## Slide 1
Benchmarking ML Anomaly Detection Methods on the Tennessee Eastman Process
Sunshine, Lyu, Botcha, Kulkarni, Pagaria, Alves, Kitchin Department of Chemical Engineering, Carnegie Mellon University

## Slide 2
Motivation
• Industrial processes require reliable fault detection and diagnosis (FDD)
• Early fault detection prevents equipment damage, safety hazards, and costly downtime
• Tennessee Eastman Process (TEP) is a widely-used benchmark in process control
• Many ML methods proposed, but fair comparison is challenging:
  - Different dataset splits
  - Varying evaluation metrics
  - No standardized benchmark

## Slide 3
Research Objectives
• Create a rigorous, reproducible benchmark for ML-based fault detection
• Compare classical ML (XGBoost) vs. deep learning approaches
• Evaluate supervised multiclass classification and unsupervised anomaly detection
• Test temporal post-processing methods (HMM filtering)
• Assess generalization to new, unseen process data

## Slide 4
Tennessee Eastman Process (TEP)
• Realistic simulation of a chemical plant with 5 major unit operations
• 52 process variables: 41 measurements + 11 manipulated variables
• 17 fault types included (3 subtle faults excluded: 3, 9, 15)
• Fault types include: step changes, random variations, slow drifts, sticking valves
• Data from Harvard Dataverse (Rieth et al., 2017)

## Slide 5
Dataset Construction
Dataset | Samples | Classes | Purpose
Multiclass Train | 864,000 | 18 | Model training
Multiclass Val | 432,000 | 18 | Hyperparameter tuning
Multiclass Test | 2,880,000 | 18 | Performance evaluation
Binary Train | 50,000 | 1 (normal) | Autoencoder training
Binary Test | 795,200 | 2 | Anomaly detection eval

## Slide 6
Dataset Key Features
• Perfectly balanced classes (standard deviation = 0.00)
• Zero data leakage: train/test from independent simulation runs
• Different fault introduction times (sample 21 vs 161)
• Strong statistical power: 95% CI width = +/-0.5%
• 160,000 test samples per class (160x larger than MNIST per class)

## Slide 7
Models Evaluated
• Supervised Multiclass:
• XGBoost (gradient boosting)
• LSTM (recurrent network)
• LSTM-FCN (LSTM + 1D CNN)
• CNN-Transformer (attention)
• TransKal (Transformer + Kalman)
• Unsupervised Binary:
• LSTM Autoencoder
• Convolutional Autoencoder
•
• Post-processing:
• HMM Classification Filter

## Slide 8
10-Series: Hyperparameter Tuning
• Optuna optimization with 50 trials per model
• Objective: Maximize weighted F1 score on validation set
• 50% training data sampling (preserving run structure)
• MedianPruner for early stopping of unpromising trials
• Total tuning time: ~49 hours

## Slide 9
Hyperparameter Tuning Results (10-Series)
Model | Best Val F1 | Tuning Time | Key Finding
XGBoost | 0.9236 | 7h 28m | max_depth=6, lr=0.20
LSTM | 0.9878 | 6h 37m | seq_len=39, layers=3
LSTM-FCN | 0.9896 | 11h 1m | seq_len=40, dropout=0.44
CNN-Transformer | 0.9890 | 8h 22m | d_model=32, 4 heads
TransKal | 0.9878 | 12h 6m | Kalman Q=5e-5, R=0.02
LSTM-AE | 0.9817 | 2h 34m | threshold=98%
Conv-AE | 0.9937 | 1h 11m | No transformer needed

## Slide 10
Key Hyperparameter Insights
• Optimal sequence length: 38-40 samples for all deep learning models
• Simpler architectures often outperformed complex ones
• Dropout varies significantly: LSTM (0.07) vs LSTM-FCN (0.44)
• Autoencoder threshold: ~98th percentile optimal for anomaly detection
• Conv-Autoencoder: Pure CNN beats CNN+Transformer hybrid

## Slide 11
Final Model Training Results (20-Series)
Model | Test Accuracy | F1 (weighted) | Training Time
LSTM-FCN | 99.37% | 0.9937 | 26m
CNN-Transformer | 99.20% | 0.9920 | 68m
LSTM | 99.14% | 0.9914 | 20m
TransKal | 99.09% | 0.9909 | 32m
XGBoost | 93.91% | 0.9416 | 40m
Conv-AE (binary) | 99.39% | 0.9939 | <1m
LSTM-AE (binary) | 96.96% | 0.9705 | 12m

## Slide 12
Training Observations (20-Series)
• Deep learning models (99%+) significantly outperform XGBoost (94%)
• LSTM-FCN achieves best multiclass accuracy (99.37%)
• Temporal models excel: sequence-based > independent samples
• Some faults perfectly classified: Classes 6, 7, 14 achieve F1 = 1.0
• Challenging classes: Normal (0), Class 12, Class 18 have lower F1

## Slide 13
30-Series: HMM Classification Filter
• Post-processing to exploit temporal consistency in predictions
• Uses confusion matrix as emission model P(observation | true_class)
• "Sticky" transition model assumes faults persist over time
• Stickiness parameter gamma tested: 0.70, 0.85, 0.95
• Resets at beginning of each simulation run

## Slide 14
HMM Filter Results (30-Series)
Model | Raw Acc | Best gamma | Filtered Acc | Error Reduction
XGBoost | 93.91% | 0.95 | 95.90% | 32.7%
LSTM | 99.14% | 0.95 | 99.14% | 0.7%
LSTM-FCN | 99.37% | 0.70 | 99.37% | 0.1%
CNN-Transformer | 99.20% | 0.95 | 99.21% | 1.2%
TransKal | 99.08% | 0.85 | 99.08% | 0.4%

## Slide 15
HMM Filter: Key Finding
• XGBoost benefits significantly: 32.7% error reduction (+2% accuracy)
• Deep learning models: <1.5% error reduction (minimal benefit)
• Reason: Deep learning already captures temporal patterns
• XGBoost treats samples independently -> needs post-hoc smoothing
• Recommendation: Use HMM for XGBoost; skip for neural networks

## Slide 16
40-Series: New Data Evaluation
• Critical test: Do models generalize to completely unseen data?
• Generated new dataset with tep-sim using different random seeds
• Same fault scenarios, same simulation parameters
• ~2M new multiclass samples, ~1.2M new binary samples
• Tests real-world deployment scenario

## Slide 17
Generalization Results (40-Series)
Model | Original Acc | New Data Acc | Change | Assessment
CNN-Transformer | 99.20% | 99.57% | +0.38% | Excellent
LSTM-FCN | 99.37% | 98.93% | -0.44% | Good
LSTM | 99.14% | 98.91% | -0.23% | Good
XGBoost | 93.91% | 89.40% | -4.51% | Poor
TransKal | 99.09% | 87.57% | -11.52% | Severe
Conv-AE | 99.39% | 76.04% | -23.35% | Failed

## Slide 18
Generalization: Key Insights
• CNN-Transformer is the ONLY model that improved on new data!
• Transformer attention learns robust, transferable patterns
• LSTM and LSTM-FCN show good robustness (<0.5% drop)
• TransKal: Kalman parameters overfit to training distribution
• Conv-Autoencoder: Threshold highly dataset-specific (needs recalibration)

## Slide 19
Final Model Rankings
Rank | Model | New Data Acc | Recommendation
1 | CNN-Transformer | 99.57% | Best for deployment
2 | LSTM-FCN | 98.93% | Good alternative
3 | LSTM | 98.91% | Simple, robust
4 | XGBoost + HMM | ~91%* | Interpretable option
5 | TransKal | 87.57% | Avoid (overfit)
6 | Conv-AE | 76.04% | Needs recalibration

## Slide 20
Conclusions
• Deep learning significantly outperforms classical ML (99% vs 94%)
• CNN-Transformer achieves best generalization (99.57% on new data)
• Temporal modeling is critical: sequence-based models excel
• HMM filtering helps XGBoost but not deep learning
• Autoencoder thresholds require recalibration for new conditions
• TransKal's Kalman filter can overfit to training distribution

## Slide 21
Practical Recommendations
• For multiclass fault classification: CNN-Transformer or LSTM-FCN
• For anomaly detection: LSTM Autoencoder (more robust than Conv-AE)
• For interpretability: XGBoost with HMM post-processing
• Always validate on held-out data from independent conditions
• Recalibrate autoencoder thresholds when process conditions change

## Slide 22
Limitations & Future Work
• Limitations:
• Perfectly balanced (unrealistic)
• No imbalanced evaluation
• 17 fault types only
• No novel fault detection
• Sample-level, not time-series metrics
• Future Work:
• Imbalanced test evaluation
• Detection delay metrics
• Novel fault generalization
• Class-wise autoencoder ensemble
• Hierarchical mixture of experts

## Slide 23
Acknowledgments
• Data: Harvard Dataverse (Rieth et al., 2017)
• Original TEP: Downs & Vogel (1993)
• Computing: Carnegie Mellon University
• Contact: jkitchin@andrew.cmu.edu